## Slide 1: Ignition Systems
Chapter #10

## Slide 2: Basic Ignition System Operation
To provide sufficient voltage to discharge a spark between the electrodes of a spark plug.

## Slide 3: Ignition System Components
Most small engine use a magneto system or variation. Magneto is specific to a points system, but is used universally to describe various ignition systems. You decide what language you want to use… Control module… Ignition module…
  Permanent magnet
  Spark plug
  Sparkplug wire
  Ignition coil
  Switching device

## Slide 4: Ignition Coil

## Slide 7: Spark Plugs

## Slide 8: Spark Plugs

## Slide 11: What is the gap?
Look it up… .023-.030 ???

## Slide 13: Spark Plug Code Interpretation

## Slide 15: Plugs???
Replace every 100 hrs. or first sign of hard starting.
Torque: Alum. head 210 in/lbs Cast iron head 300 in/lbs
Battered or clogged threads M14 X1.25 metric tap
Heli-coil - Thread insert

## Slide 16: Plug Brand?
Briggs uses Champion.
I use NGK or Bosch.
What will you use?

## Slide 17: Spark Plug Heat Transfer
Heat range

## Slide 18: Spark Plug Wire

## Slide 20: Switching Devices
Trigger collapsing field in primary coil – inducing a high voltage in secondary coil – firing plug – igniting fuel/air mixture – driving piston down on power stroke
Mechanical
Electronic

## Slide 21: Flywheel - it’s magnetic…

## Slide 22: Removal - Flywheel
Starter drive – tool 19163
Puller
Shocker

## Slide 23: Key and keyway
Briggs uses soft aluminum
Other manufactures use steel
Replace flywheel or hub
if worn.
Magnets seldom wear out.
Should attract screwdriver
5/8”away.
CDI uses weaker magnets.

## Slide 24: Installing Flywheel
Clean crankshaft
Bellville washer convex side up
30 wt. oil on bolt threads
Torque
  Engines >6 CID – 40 ft/lbs
  6 to 10 CID – 55 to 60 ft/lbs
  11 to 20 CID – 85 to 90 ft/lbs

## Slide 28: Use a business card

## Slide 29: Magneto Ignition Systems

## Slide 32: Capacitive Discharge Ignition (CDI)

## Slide 33: CDI Ignition…
Do not run with battery disconnected…
Kohler Smart Spark CDI
Do not run with plug wire disconnected.

## Slide 34
Flywheel magnets generate 200 VAC in the input coil
The Rectifier converts the AC output to DC storage in the capacitor
The SCR (silicon controlled rectifier) remains non-conductive to block capacitor discharge
About 180 degrees later flywheel magnet sweeps past the trigger coil to generate signal voltage across the resistor – this causes the SCR the conduct
The stored charge on the capacitor discharges through the primary side of the pulse transformer
Current flow in the primary side of the pulse transformer (actually the ignition coil) generates a 25K Volt potential in the secondary windings that goes to ground across the spark-plug electrodes
Caution: Solid-state components are vulnerable to stray and reversed-polarity voltage

## Slide 35: Troubleshooting
Replace plug
Replace key is distorted or sheared
Check wiring, dielectric grease on contentions
Ignition interlock
Test unit (special tool) or replace with know good unit

## Slide 36: Transistor-Controlled Ignition (TCI)
Magnetron
Plug terminal and engine
ground 3K – 5K Ohms.

## Slide 37: Darlington Transistor Used for amplification…

## Slide 38: Mechanical Breaker Point Ignition (MBI)m

## Slide 42
Test ign. Circuit
W or W/O plug

## Slide 44: MSD
The MSD Enhancer system for the Briggs & Stratton/Tecumseh is designed as a complete system. The system has 12 Volts DC operating voltage, 14,000 (1 Cylinder) rpm range, 100 MJ energy output maximum, 14° – 18° (1 Cylinder) multi spark duration, 1.5 AMPS @ 10,000 RPM current requirements, Primary 450 Volts voltage output, and 30,000+ VOLTS with MSD Coil secondary voltage. The following schematic shows the MSD Briggs & Stratton/Tecumseh Ignition System Wiring Diagram.

## Slide 45: Battery Ignition Systems
Textbook pages 208-209
  Figure 10-24, 10-25, & 10-26

## Slide 46: The Lead-Acid Battery
6 cells, each cell 2.105V
Discharge rate 3-20% month
500-800 cycles

## Slide 47: Batteries Cont.
Explosion – Hydrogen
Recycling
Baking soda or ammonia
Sulfating and DE sulfating
Types of Batteries
State of Charge | Specific Gravity | Voltage | 
 |  | 12V | 6V
100% | 1.265 | 12.7 | 6.3
75% | 1.225 | 12.4 | 6.2
50% | 1.190 | 12.2 | 6.1
25% | 1.155 | 12.0 | 6.0
Discharged | 1.120 | 11.9 | 6.0

## Slide 49: Electrical System Simplified